## Slide 1: Smart Home
Mohamed Mohamed Mohamed Hassen Q9-Online
Yousef Mohamed Mohamed Ahmed Q9-Online
Mohamed Orabeya Q9-Online

## Slide 2: Outlines
Problem statement
Problem solving
System construction
System instruction
Flow chart
Architecture
Simulation
GitHub Repo Link

## Slide 3: Problem statement
Our traditional homes are suffers from lack in communication between the home and its resident.
No feedback if something went wrong as:
The door is closed or not .
Fire alert during work.
Forgetting the Ac on for a long time.
Anonymous person enters the home while you not existing there.

## Slide 4: Problem solving
Smart home is the brilliant solution for all the previous information.
Smart home provide an access to the resident to check the at anytime & everywhere.
Smart home includes some sensors that fix the previous problems:
Door sensor: to check whether the door is closed or not.
Fire sensor is connected to LAN network to give you a mobile alert notification.
Schedule notification to remind you that the AC is working.
Internal cameras and sensors to avoid theft.

## Slide 5: System construction
System is consists of 2 microcontroller an Bluetooth module.
Our system is based on Bluetooth connection between a mobile device and master microcontroller.
Master microcontroller send instruction to the slave one.
The sent instruction is based on the instruction sent by the user via Bluetooth.

## Slide 6: System construction
Mobile device
Bluetooth module
Master
Microcontroller
Slave
Microcontroller
SPI connection
Send instruction
Via Bluetooth
Send
instruction
Via UART
Do instruction

## Slide 7: System instruction
System has 2 outputs: AC and light system.
Output form is based on the instruction sent from mobile device.
Instructions are:
TURN AC ON ONLY.
TURN AC OFF ONLY.
TURN LIGHT ON ONLY.
TURN LIGHT OFF ONLY.
TURN ON BOTH.
TURN OFF BOTH.

## Slide 8: System instruction
Instructions description :
TURN AC ON ONLY : master send address 0x10 to slave microcontroller, so the slave microcontroller will turn on the AC only.
TURN AC OFF ONLY : master send address 0x20 to slave microcontroller, so the slave microcontroller will turn off the AC only.
TURN LIGHT ON ONLY : master send address 0x30 to slave microcontroller, so the slave microcontroller will turn on the light only.
TURN LIGHT OFF ONLY : master send address 0x40 to slave microcontroller, so the slave microcontroller will turn off the light only .
TURN ON BOTH : master send address 0x50 to slave microcontroller, so the slave microcontroller will turn on both AC and light.
TURN OFF BOTH : master send address 0x60 to slave microcontroller, so the slave microcontroller will turn off both AC and light.

## Slide 9: Architecture
Our design based on layered Architecture for each microcontroller.
Master microcontroller has 3 software module of MCAL(microcontroller abstraction layer):
Input / output module.
SPI module.
UART module
Slave microcontroller has 2 software module of MCAL (microcontroller abstraction layer):
Input / output module.
SPI module.

## Slide 10: Flow chart

## Slide 11: Flow chart

## Slide 12: Architecture
Each software module is composed of 3 files:
Private.h (contains private information that can’t be shared with the user).
Interface.h (contains information as prototypes, macros & function used).
Program.h (contains main logic of the used functions).
The main code includes the interface files of each module in order to be called.

## Slide 13: Simulation
System simulation is done by PROTEUS simulation in order to test whole the system. (check the PROTEUS file for real-time simulation)

## Slide 14: GitHub Repo Link
Mohamed Hassen’s link:
https://github.com/Muhamed1470/smart-home.git
Yousef Mohamed’s link:
https://github.com/yousefmohammed98/smart-home.git
Mohamed Orabeya’s link:
https://github.com/Orabya/Smart-home.git